## Slide 1
KAUST Network
Server(Harbor)
10.185.179.41
Client(Campus)
10.68.75.53
Ethernet
KAUST Network
Server(Harbor)
10.240.136.29
Client(Campus)
10.68.75.53
Ethernet
WIFI
Ethernet
It's easy to understand that wired channel has better bandwidth due to the worse noisy for wireless signal as well as the multiple user for iCampus WIFI.
Different Interface
Da LI

## Slide 2
Different locations
Speedtest2 and Speedtest3
  Features:
    Have same claimed speed
    Small difference
    Close location
  Difference:
    Speedtest3 has heavier traffic
Uztelecom
  Features:
    Have same claimed speed
  Difference:
    Some bad router nodes(Tracert)
Da LI

## Slide 3
The length of buffers to read or write. iPerf works by writing an array of len bytes a number of times. Default is 128 KB for TCP, 8 KB for UDP.
Different Bufferlen
Smaller buffers:
increase system overhead
cause throughput fluctuations
Larger buffers:
reduce system calls
improving throughput stability and efficiency
especially in high-bandwidth networks.(Unless reach the limit of the network)
Da LI

## Slide 4
Goodput
Da LI

## Slide 5
Owamp
Da LI

## Slide 6: Question
Why we have negative delay value from owamp? What’s the err time? If the delay time plus or minus the err time equal to the real delay?
Why the one way delay is totally different the round trip time(RTT) from ping tool?
rtt min/avg/max/mdev = 1.313/2.066/2.868/0.468 ms
delay min/median/max = -30.9/-30.4/-15.9 ms
delay min/median/max = 32.3/32.6/32.7 ms, (err=1.55 ms)